Argos Froyanes Gear details Line type Autoline Line material 12 mm thick Polyester/polypropylene mix Average line length and range 6,708 m (4,500 – 10,800) Hook type EZ 14/0 straight shank Number of hooks per line and spacing2 4,472 (3,000 – 7,200) at 1.5 m spacing Snood Length 0.4m Weight material and mass Integrated weight, 50 g/m Spacing of weights N/A Sink rate 0.37m/s Anchor type and number One 65/80kg grapnel anchor and one 40/45kg chain at either end. Floats and spacing N/A The vessel uses two different gear configurations depending on the topography of the fishing grounds and the ice conditions, single lines and join lines, as illustrated above.

| Type | Straight shank |
| --- | --- |
| Make | Fiskevegn |
| Total length | 78 |
| Shank (mm) | 45 |
| Gape (mm) | 16 |
| Throat (mm) | 33 |
| Front length (mm) | 35 |
| Usual setting position |
| Line off bottom (m) | 0 |
| Hooks off bottom (m) | 0 |

# Footnotes

Based on 2018/19 data from Argos Froyanes.

For regular gear, measurement of sink rates is no longer required, data are from 2014/15 season from Argos Froyanes.